fft      from ulib                                     08/02/85
 package fft            description of individual user entries
                        follows the package description below.

 latest revision        january 1985

 purpose                fast fourier transforms for data of arbitrary
                        length.  the file fft contains three routines
                        to handle various forms of input data as
                        tabulated below:
                          routine name  input form     output form
                          ------------  ----------     -----------
                             fftrc         real        half complex
                             fftcr      half complex      real
                             fftcc        complex        complex

                        half complex refers here to the first n/2+1
                        complex values of a conjugate symmetric array
                        of length n.

 special conditions     the efficiency of these routines is greatly
                        affected by the number of points to be
                        transformed.  if n is the length of the
                        transform (nrlpts in fftrc or fftcr; ncpts in
                        fftcc) the execution time is roughly
                        proportional to n*sumpf where sumpf is the sum
                        of the prime factors of n.  clearly, numbers
                        with large prime factors should be avoided.
                        if n is a power of two, the package fftpow2
                        provides greater efficiency.

 i/o                    error messages are printed by routine uliber.

 precision              single

 required library       uliber and q8qst4, which are loaded by
 files                  default on ncar's cray machines.

 language               fortran

 history                developed at ncar by dave fulker of the
                        scientific computing division in the early
                        1970's.

 portability            fortran 66
***********************************************************************

 subroutine fftrc(rldat,nrlpts,signex,hctrn,nhcpts,work,lwrk,ierr)

 dimension of           real rldat (nrlpts)
 arguments              complex hctrn (nhcpts)
                          where nhcpts = nrlpts/2+1
                        real work (lwrk)

 purpose                fourier transform (real to half complex).  (in
                        case signex = +1., the computation performed by
                        this routine is sometimes called a forward
                        transform or fourier analysis.)  the discrete
                        fourier transform of an array rldat, containing
                        nrlpts real values, is a set cf of nrlpts
                        complex values satisfying the conjugate
                        symmetry relation cf(nrlpts+2-k) = conjg(cf(k))
                        (k = 2,nrlpts).  due to this symmetry relation,
                        it is only necessary to compute the first
                        nhcpts = nrlpts/2+1 complex values, and these
                        are returned in the complex array hctrn.

 usage                  call fftrc (rldat,nrlpts,signex,hctrn,nhcpts,
                                    work,lwrk,ierr)
                          the original values of rldat may be
                          regenerated from hctrn by first dividing all
                          values of hctrn by nrlpts and then calling
                          fftcr (hctrn,nhcpts,-signex,rldat,nrlpts,
                                 work,lwrk,ierr).

 arguments

 on input               rldat
                          a real array containing the nrlpts data
                          values to be transformed.

                        nrlpts
                          the number of real data values to be
                          transformed.  for the greatest efficiency, it
                          should be a product of small primes.

                        signex
                          a variable whose sign determines the sign of
                          the argument of the complex exponential used
                          in the transform computations.  for
                          convenience, we assume in these comments that
                          signex is +1. or -1., but the routine in fact
                          only uses the sign of its value.

                        nhcpts
                          the number of complex values to be returned
                          as the half complex transform result in array
                          hctrn.  it must be = nrlpts/2+1 or a fatal
                          error is flagged.
                          note:  nhcpts is not an output parameter.  it
                                 must be set to nrlpts/2+1 by the user,
                                 and nhcpts complex locations must be
                                 provided for the output array hctrn.

                        work
                          a workspace of length lwrk (.ge. 4*nrlpts)
                          for use by the routine.

                        lwrk
                          the length of array work.  it must be
                          .ge. 4*nrlpts or a fatal error is flagged.

 on output              hctrn
                          the complex array containing the
                          first half of the conjugate symmetric
                          transform result.  these values are
                          referred to as fourier coefficients.

                          assume signex = +1. or -1. and cex(x)
                          (for real x) is the complex exponential
                          of signex*2*pi*i*x/nrlpts  where pi = 3.14...
                          and i = sqrt(-1.).

                          then (for k = 1,nhcpts)
                            hctrn(k) =  sum   rldat(j)*cex((j-1)*(k-1)
                          where the sum index is j = 1,....nrlpts.

                        work
                          workspace containing intermediate results.

                        ierr
                          an error flag with the following meanings:
                          =   0  no error.
                          = 101  nrlpts is less than 1.
                          = 102  nhcpts is not nrlpts/2+1.
                          = 103  insufficient workspace has been
                                 provided; lwrk is less than 4*nrlpts.
***********************************************************************

 subroutine fftcr (hcdat,nhcpts,signex,rltrn,nrlpts,work,lwrk,ierr)

 dimension of           complex hcdat (nhcpts)
 arguments              real rltrn (nrlpts)   where nrlpts/2+1 = nhcpts
                        real work (lwrk)

 purpose                fourier transform (half complex to real).  (in
                        case signex = -1., the computation performed by
                        this routine is sometimes called a backward
                        transform or fourier synthesis.) hcdat is
                        assumed to be the first nhcpts = nrlpts/2+1
                        complex values of a set cf containing nrlpts
                        complex values which satisfy the conjugate
                        symmetry relation cf(nrlpts+2-k) = conjg(cf(k))
                        (k = 2,nrlpts).  in addition, hctrn(1) is
                        assumed to be real.  the discrete fourier
                        transform of such a conjugate symmetric array
                        is a set of nrlpts real values which are
                        returned in the real array rltrn.

 usage                  call fftcr (hcdat,nhcpts,signex,rltrn,nrlpts,
                                    work,lwrk,ierr)
                          the original values of hcdat may be
                          regenerated from rltrn by first dividing all
                          values of rltrn by nrlpts and then calling
                          fftrc (rltrn,nrlpts,-signex,hcdat,nhcpts,
                                 work,lwrk,ierr).

 arguments

 on input               hcdat
                          a complex array containing nhcpts complex
                          values which comprise essentially the first
                          half of the conjugate symmetric data to be
                          transformed.

                        nhcpts
                          the number of complex values entered in
                          hcdat.

                        signex
                          a variable whose sign determines the sign of
                          the argument of the complex exponential used
                          in the transform computations.  for
                          convenience we assume in these comments that
                          signex is +1. or -1., but the routine in fact
                          only uses the sign of its value.

                        nrlpts
                          the number of real transform values to be
                          returned.  nhcpts must be nrlpts/2+1 or a
                          fatal error is flagged.
                          note:  nrlpts is not an output parameter.  it
                                 must satisfy nrlpts/2+1 = nhcpts, and
                                 nrlpts real locations must be provided
                                 for the output array rltrn.

                        work
                          a workspace of length lwrk (.ge. 4*nrlpts)
                          for use by the routine.

                        lwrk
                          the length of array work.  it must be
                          .ge. 4*nrlpts or a fatal error is flagged.

 on output              rltrn
                          real array containing transform result.

                          assume signex = +1. or -1. and cex(x)
                          (for real x) is the complex exponential
                          of signex*2*pi*i*x/nrlpts  where pi = 3.14...
                          and i = sqrt(-1.).

                          then for j = 1,...,nrlpts
                            rltrn(j) =  sum   cf(k)*cex(j-1)*(k-1))
                          where the sum index is k = 1,...,nrlpts
                          and where
                            cf(k) = hcdat(k)/nrlpts
                                    for 1 .le. k .le. nhcpts
                                  = conjg(cf(nrlpts+2-k))
                                    otherwise

                        work
                          workspace containing intermediate results.

                        ierr
                          an error flag with the following meanings:
                            0  no error.
                          101  nrlpts is less than 1.
                          102  nhcpts is not nrlpts/2+1.
                          103  insufficient workspace has been
                               provided:  lwrk is less than 4*nrlpts.
***********************************************************************

 subroutine fftcc (cdata,ncpts,signex,ctran,work,ierr)

 dimension of           complex cdata (ncpts),ctran (ncpts)
 arguments              real work(2*ncpts)

 purpose                fourier transform (complex to complex).  (in
                        case signex = +1., the computation performed by
                        this routine is sometimes called a forward
                        transform or fourier analysis.  for
                        signex = -1., it is called a backward transform
                        or fourier synthesis.)  the discrete fourier
                        transform of an array cdata, containing ncpts
                        complex values, is a set of ncpts complex
                        values which are returned in the complex array
                        ctran.

 usage                  call fftcc (cdata,ncpts,signex,ctran,work,ierr)
                          the original values of cdata may be
                          regenerated from ctran by first dividing all
                          values of ctran by ncpts and then calling
                          fftcc (ctran,ncpts,-signex,cdata,work,ierr).

 arguments

 on input               cdata
                          a complex array containing the ncpts complex
                          data values to be transformed.

                        ncpts
                          the number of complex data values to be
                          transformed.  it must be a positive power of
                          2 or a fatal error is flagged.

                        signex
                          a variable whose sign determines the sign of
                          the argument of the complex exponential used
                          in the transform computations.  for
                          convenience, we assume in these comments that
                          signex is +1. or -1., but the routine in fact
                          only uses the sign of its value.

                        work
                          a workspace of length 2*ncpts for use by the
                          routine.

 on output              ctran
                          the complex array of length ncpts
                          containing the transformed results.
                          these values are also referred to as the
                          fourier coefficients.

                          assume signex = +1. or -1. and cex(x)
                          (for real x) is the complex exponential
                          of signex*2*pi*i*x/nrlpts  where pi = 3.14...
                          and i = sqrt(-1.).

                          for k = 1,ncpts
                            ctran(k) =  sum  cdata(j)*cex(j-1)*(k-1))
                          where the sum index is j = 1,...,ncpts.

                        work
                          workspace containing intermediate results.

                        ierr
                          an error flag with the following meanings:
                            0  no error.
                          101  ncpts is less than 1.
******************************************************************************

  fourt


     the cooley-tukey fast fourier transform in usasi basic fortran

     transform(j1,j2,,,,) = sum(data(i1,i2,,,,)*w1**((i2-1)*(j2-1))
                                 *w2**((i2-1)*(j2-1))*,,,),
     where i1 and j1 run from 1 to nn(1) and w1=exp(isign*2*pi=
    sqrt(-1)/nn(1)), etc.  there is no limit on the dimensionality
     (number of subscripts) of the data array.  if an inverse
     transform (isign=+1) is performed upon an array of transformed
     (isign=-1) data, the original data will reappear.
     multiplied by nn(1)*nn(2)*,,,  the array of input data must be
     in complex format.  however, if all imaginary parts are zero (i.e.
     the data are disguised real) running time is cut up to forty per-
     cent.  (for fastest transform of real data, nn(1) should be even.)
     the transform values are always complex and are returned in the
     original array of data, replacing the input data.  the length
     of each dimension of the data array may be any integer.  the
     program runs faster on composite integers than on primes, and is
     particularly fast on numbers rich in factors of two.

     timing is in fact given by the following formula.  let ntot be the
     total number of points (real or complex) in the data array, that
     is, ntot=nn(1)*nn(2)*...  decompose ntot into its prime factors,
     such as 2**k2 * 3**k3 * 5**k5 * ...  let sum2 be the sum of all
     the factors of two in ntot, that is, sum2 = 2*k2.  let sumf be
     the sum of all other factors of ntot, that is, sumf = 3*k3*5*k5*..
     the time taken by a multidimensional transform on these ntot data
     is t = t0 + ntot*(t1+t2*sum2+t3*sumf).  on the cdc 3300 (floating
     point add time = six microseconds), t = 3000 + ntot*(600+40*sum2+
     175*sumf) microseconds on complex data.

     implementation of the definition by summation will run in a time
     proportional to ntot*(nn(1)+nn(2)+...).  for highly composite ntot
     the savings offered by this program can be dramatic.  a one-dimen-
     sional array 4000 in length will be transformed in 4000*(600+
     40*(2+2+2+2+2)+175*(5+5+5)) = 14.5 seconds versus about 4000*
     4000*175 = 2800 seconds for the straightforward technique.

     the fast fourier transform places three restrictions upon the
     data.
    1.  the number of input data and the number of transform values
     must be the same.
     2.  both the input data and the transform values must represent
     equispaced points in their respective domains of time and
     frequency.  calling these spacings deltat and deltaf, it must be
     true that deltaf=2*pi/(nn(i)*deltat).  of course, deltat need not
     be the same for every dimension.
     3.  conceptually at least, the input data and the transform output
     represent single cycles of periodic functions.

     the calling sequence is--
     call fourt(data,nn,ndim,isign,iform,work)

     data is the array used to hold the real and imaginary parts
     of the data on input and the transform values on output.  it
     is a multidimensional floating point array, with the real and
     imaginary parts of a datum stored immediately adjacent in storage
     (such as fortran iv places them).  normal fortran ordering is
     expected, the first subscript changing fastest.  the dimensions
     are given in the integer array nn, of length ndim.  isign is -1
     to indicate a forward transform (exponential sign is -) and +1
     for an inverse transform (sign is +).  iform is +1 if the data are
     complex, 0 if the data are real.  if it is 0, the imaginary
     parts of the data must be set to zero.  as explained above, the
     transform values are always complex and are stored in array data.
     work is an array used for working storage.  it is floating point
     real, one dimensional of length equal to twice the largest array
     dimension nn(i) that is not a power of two.  if all nn(i) are
     powers of two, it is not needed and may be replaced by zero in the
     calling sequence.  thus, for a one-dimensional array, nn(1) odd,
     work occupies as many storage locations as data.  if supplied,
     work must not be the same array as data.  all subscripts of all
     arrays begin at one.

     example 1.  three-dimensional forward fourier transform of a
     complex array dimensioned 32 by 25 by 13 in fortran iv.
     dimension data(32,25,13),work(50),nn(3)
     complex data
     data nn/32,25,13/
     do 1 i=1,32
     do 1 j=1,25
     do 1 k=1,13
  1  data(i,j,k)=complex value
     call fourt(data,nn,3,-1,1,work)

     example 2.  one-dimensional forward transform of a real array of
     length 64 in fortran ii,
     dimension data(2,64)
     do 2 i=1,64
     data(1,i)=real part
  2  data(2,i)=0.
     call fourt(data,64,1,-1,0,0)

     there are no error messages or error halts in this program.  the
     program returns immediately if ndim or any nn(i) is less than one.

     program by norman brenner from the basic program by charles
     rader,  june 1967.  the idea for the digit reversal was
     suggested by ralph alter.

     this is the fastest and most versatile version of the fft known
     to the author.  a program called four2 is available that also
     performs the fast fourier transform and is written in usasi basic
     fortran.  it is about one third as long and restricts the
     dimensions of the input array (which must be complex) to be powers
     of two.  another program, called four1, is one tenth as long and
     runs two thirds as fast on a one-dimensional complex array whose
     length is a power of two.

     reference--
     ieee audio transactions (june 1967), special issue on the fft.